## Slide 1: Parallel simulation of SystemC TLM 2.0 LT models
Master Thesis Internship
Konstantinos Sotiropoulos
kisp@kth.se

## Slide 2: Problem statement
Parellel execution must be carefully orchestrated to preserve causality
Causality demands Synchronization
“This project evaluates the efficiency of existing process synchronization algorithms when applied to the parallel simulation of Loosely-Timed Transaction Level Models.”

## Slide 3: Motivation
Poor simulation performance often constraints the scope and depth of design decisions that can be evaluated
Extend the literature for TLM modeling

## Slide 4: Objectives
Document
        Intermediate report available
Synchronization algorithms for PDES:
        Chandy-Misra-Bryant family of conservative synchronization algorithms
A programming framework for expressing the parallel simulation:
        Intel MPI
A recoding infrastructure able to generate both TLM and MPI version:
        XML representation of the system using a library of TLM components
A pragmatic Transaction Level Model to experiment on.
      Simulating en tandem Hardware and Software.

## Slide 5: TLM loosely-timed diagram semantics
Figure 1: Semantics of TLM LT diagram

## Slide 6: System
Figure 2: A Shared Memory, Cache-Coherent, Symmetric Multiprocessor based on the OpenRisc ISS

## Slide 7: System behavior (Read Miss)
Figure 3: A sequence diagram indicating component interaction in case of L1 & L2 cache read miss

## Slide 8: The CMB synchronization algorithm
Each process keeps a local time which corresponds to the timestamp of the last event processed.
For every incoming link, a process selects the event with the smallest timestamp.
When an incoming link is empty, the process blocks.
After processing an event, a process provides an event in every outgoing link. Either a meaningful payload, or a null value with a timestamp. The timestamp is the process’ local time plus a lookahead.
Figure 4: Transforming a TLM system to process network

## Slide 9: Message Passing Interface in a nutshell
Basic primitives: MPI_Send(), MPI_Recv()
Basic arguments: the peer process’ id and a data buffer
Each process has its own address space.
Message transmission consists of three phases:
    Data is pulled out of the send buffer and a message is assembled
    A message is transferred from sender to receiver
    Data is pulled from the incoming message FIFO and disassembled into the receive buffer

## Slide 10: The CMB algorithm in MPI
while local_time < sim_end do
1. MPI_Irecv(...) on every empty incoming link
2. MPI_Wait(...) until every receive has been completed
3. identify message M with the smallest timestamp
4. set local_time = timestamp(M)
5. process message M (using function registered as b_transport)
6. MPI_Bsend(...) on every outgoing link
end
Figure 5: CMB Process event loop in MPI

## Slide 11: Hypotheses
Cache Coherence messages will facilitate the diffusion of computation.
We can use the memory hierarchy’s time penalties as lookaheads
For an application with an arithmetic intensity above a certain threshold we should observe a significant speed up against the SystemC TLM simulation
Unfortunately, no conclusive result has been reached...

## Slide 12
February | 5 | Project Plan |  | July | 26 | Vacations |  | 
 | 6 |  |  |  | 27 |  |  | 
 | 7 |  |  |  | 28 | MPI model |  | 
 | 8 | Xeon Phi Administration |  |  | 29 |  |  | 
March | 9 |  |  |  | 30 |  |  | 
 | 10 | CMB in MPI |  | August | 31 | Simulation Data |  | 
 | 11 |  |  |  | 32 | Draft of Final Report |  | 
 | 12 | ISS |  |  | 33 |  |  | 
 | 13 |  |  |  | 34 |  |  | 
April | 14 |  |  | September | 35 | Defence of thesis |  | 
 | 15 | Intermediate Report |  |  | 36 | Finalize Report |  | 
 | 16 |  |  |  |  |  |  | 
 | 17 |  |  |  |  |  |  | 
May | 18 |  |  |  |  |  |  | 
 | 19 | Modeling Cache Hierarchy |  |  |  |  |  | 
 | 20 |  |  |  |  |  |  | 
 | 21 | KTH Exams + Week off |  |  |  |  |  | 
June | 22 |  |  |  |  |  |  | 
 | 23 | Testing Cache Hierarchy |  |  |  |  |  | 
 | 24 |  |  |  |  |  |  | 
 | 25 | Integration testing (TLM model) |  |  |  |  |  |